## Slide 1: CENG 232
Xilinx Installation
And
Basic Properties

## Slide 2: Hardware Description Language
Designing schematics wire by wire is:
  Hard
  Error-prone
  Gets more complex as project gets bigger
HDL
  Describe your circuits as textual “code”, just like any programming language
  Divide larger projects into smaller modules
  Harder to visualize, but easier to manage

## Slide 3: Hardware Description Language
Two popular languages:
  VHDL
    Complex at initial glance
    Provides better control when synthesizing to physical elements
Verilog
  Simpler syntax
  Easier to learn

## Slide 4: Modules
Modules
Modules are the building blocks of Verilog designs
  Inputs
  Outputs
  Semantics between inputs and outputs

## Slide 5: Testbench Idea
HDLs provide you a way to write modules
  with their inputs and outputs
How to test it?
  Create a test-module
    instantiates your own module
    writes to your module's inputs
    reads from your module's outputs
  Connect inputs and outputs of the test module to your module
  Run the testbench

## Slide 6: Testbench Idea
Testbench modules
  No inputs, no outputs (as connections)
  Access to screen, keyboard, time
  Access to tested module instance

## Slide 7: Testbench Idea
Same as plugging a chip to a physical test board which tests various inputs and blinks green light if everything is OK.
You don't have to blink a green light:
  HDLs provide a way to write to screen:
    TEST1 passed
    TEST2 failed
    TEST3 passed
    …

## Slide 8: A Simple Verilog Example
module binary_to_eseg(
input A, E input B,
input C,
input D,
output eSeg
);
wire p1, p2, p3, p4;
nand2 g1(p1, C, ~D);
nand2 g2(p2, A, B);
nand2 g3(p3, ~B, ~D);
nand2 g4(p4, A, C);
nand4 g5(eSeg, p1, p2, p3, p4);
endmodule

## Slide 9: Tools
Xilinx ISE WebPack (version 12.4)
  Integrated Development Environment
  Editor, compiler, simulator, FPGA programmer
  Linux & Windows
Free to use
  Installation requires free registration and obtaining free license.
www.xilinx.com
We will use Xilinx version 12.4, please don't use other versions

## Slide 10: Installation

## Slide 11: Installation (Cont.)

## Slide 12: Installation (Cont.)

## Slide 13: Installation (Cont.)

## Slide 14: Installation (Cont.)

## Slide 15: Installation (Cont.)

## Slide 16: Installation (Cont.)

## Slide 17: Installation (Cont.)

## Slide 18: Installation (Cont.)

## Slide 19: Creating Project
Open ISE Design Tools  Project Navigator
Create new project with the following options

## Slide 20: Basic Properties of Xilinx
2 Design modes:
  Implementation
  Simulation
Top
  Module hierarchy
Bottom
  Actions with
  Selected module

## Slide 21: Basic Properties of Xilinx
You can switch between Design and Files views
A file may belong to:
  Implementation only
    files related with FPGA board
  Simulation only
    Testbenches …
  Both
    Your design

## Slide 22: Compiling, checking syntax errors
Choose desired module
  All dependencies will also be compiled
  Compiler output will be shown in the bottom
In implementation mode
  Double click on Synthesize
OR in simulation mode
  Double click on Behavioral Check Syntax

## Slide 23: Simulation
Special commands can be used inside simulation source-files:
  $finish,$stop,$monitor,$display,..
Results of these are seen on output panel
Also, wire values of any module can be seen in timing diagram panel

## Slide 24: Simulation (Cont.)
In simulation mode
Select testbench module
Double click on Simulate Behavioral Model
  Dependencies will be compiled
  ISim Simulator will be opened

## Slide 25: Isim Simulator